Computer Systems B
COMS20012
Introduction to Operating Systems and Security

---
I/O Devices

---
Devices
Devices is how computer receive inputs and outputs
  - Keyboard is an input device
  - Printer is an output device
  - Touch Screen is both input and output
Sys161 have the following devices
  - Timer/clock
  - Disk
  - Serial Console
  - Text Screen
  - Network interface

---
Terminology
Bus: communication pathway between devices in a computer
  - Internal bus: bus between the CPU and the RAM. Relatively fast!
  - Peripheral: or extension bus, allow devices within the computer to communicate
Bridge: connects two different buses

---
Device Register
Communication with devices carried through device registers
Three primary types of registers:
  - Status: tells you about the state of a device
  - Command: issue a command to the device by writing a particular value
  - Data: used to transfer larger block of data
Some device registers can be combination of primary types:
  - Status and command: read for device state, write for command

---
Device register: Sys161 example clock
Offset	Size	Type	Description
0	4	status	current time (seconds)
4	4	status	current time (nanoseconds)
8	4	command	restart-on-expiry
12	4	status and command	interrupt (reading clears)
16	4	status and command	countdown time (microseconds)
20	4	command	speaker (causes beeps)

---
Device register: Sys161 example serial console
Offset	Size	Type	Description
0	4	command and data	character buffer
4	4	status	Read IRQ
8	4	status	Write IRQ
IRQ: interrupt request

---
Device driver
Part of the kernel that interface with a device
Example write a character to the serial console
  1. wait(console_semaphore) # only one write at a time
  1. write to character buffer
  1. while(writeIRQ!=completed)
  1. write writeIRQ to acknowledge completion
  1. signal(console_semaphore)
Polling approach
  - Check repeatedly the status of the device

---
Device driver
Polling is bad (waste CPU cycles)
Instead we should rely on interrupts
Write operation
  1. wait(console_semaphore)
  1. write to character buffer
Interrupt Handler for serial device
  1. write writeIRQ to acknowledge completion
  1. signal(console_semaphore)

---
Accessing device registers
How can our driver access device registers?
  - Option 1: port-mapped I/O with special instructions
    - Device are assigned port numbers which corresponds to an address in a separate smaller address space
    - Special instruction to read/write to this address space (in/out on x86)
  - Option 2: memory-mapped I/O
    - Each device registers associated to a physical memory address
    - This is not mapped to user space virtual addresses!
    - Read/write using normal load/store instructions (as reading/writing to normal memory)
  - An architecture can have both

---
Sys161 example
RAM
ROM
0x1FC00000 − 0x1FDFFFFF
0xFFFFFFFF
0x00000000
Devices: 0x1FE00000 − 0x1FFFFFFF
64kb device slot
Each device is assigned one
of 32 device slot.
Device registers and buffers
are mapped in the slot.
…
0x1FE00000
0x1FFFFFFF

---
Large data transfer
Write bytes one by one in register won’t be very efficient
  - Think of a hard drive
Buffer in memory
Two strategy for transfer
  - Program-controlled I/O
    - The device driver move data between the CPU and I/O device
    - The CPU is Busy
  - Direct memory access DMA
    - The device itself copy the data from memory to itself
    - The CPU is not busy while this happen
    - The device will trigger an interrupt when done
Sys161 disks use program-controlled I/O

---
Platter
R/W heads
Spindle
[Speaker Notes: Note that the platters are double-sided, i.e., they store data on both sides. Also note that all of the read/write heads move together, in unison.]

---
Cylinder
Cylinder
group
Track
Sector
[Speaker Notes: For a long time, hard disks used a sector size of 512. However, modern disks now use a sector size of 4K.]

---
Cylinder group to blocks
Cylinder groups are divided into blocks
Blocks can be addressed to read/write from disk
You can check the textbook for discussion on optimization around reading/writing from hard drive
  - 6.1.2 (page 223)
  - 6.1.3 (page 226), first finish all videos
  - Not mandatory, just if you are curious

---
Device register: Sys161 disk controller
Offset	Size	Type	Description
0	4	status	number of sectors
4	4	status and command	status
8	4	command	sector number
12	4	status	rotational speed
32768	512	data	transfer buffer

---
Writing to a Sys161 disk
Device driver
  1. wait(disk_semaphore)
  1. copy data from memory to transfer buffer
  1. write target sector to sector register
  1. write "write" command to disk status register
  1. wait(disk_completion)
  1. signal(disk_semaphore)
Interrupt handler
  1. write disk status register to acknowledge completion
  1. signal(disk_completion)

---
Reading from a Sys161 disk
Device driver
  1. wait(disk_semaphore)
  1. write target sector to sector register
  1. write “read" command to disk status register
  1. wait(disk_completion)
  1. copy data from buffer to memory
  1. signal(disk_semaphore)
Interrupt handler
  1. write disk status register to acknowledge completion
  1. signal(disk_completion)

---
Thank you