Computer Systems B
COMS20012
Introduction to Operating Systems and Security

---
Why virtual memory?

---
Physical Memory
Physical addresses are P bits long
  - Maximum amount of addressable physical memory is 2P
OS161’s MIPS is 32 bits
  - 232 physical addresses
  - Maximum of 4GB memory
Modern CPU support large amount of addressable memory
  - X86_64
  - Physical 52 bits
  - Virtual 48 bits
Far exceed current RAM technology
  - This won’t be true forever ;)

---
Physical Memory
Is finite
Need to be shared between all processes
Need to be carefully managed to avoid processes stepping on each other toes
Classic OS solution: hide complexity through an abstraction

---
Virtual Memory the basic
The kernel provide a virtual memory for each process
Virtual memory hold code, data and stack(s) for a process
If virtual memory addresses are V bits
  - Amount of addressable virtual is 2V
  - On OS161/MIPS V=32
Running processes see only virtual memory
  - Program counter and stack pointer hold virtual addresses
  - Pointers to variable are virtual addresses
  - Jumps/branches refers to virtual addresses
Each process is isolated in its virtual memory and cannot address other processes virtual memory

---
Why virtual memory?
Isolate processes from each other
Potentially to support virtual memory larger than physical memory
Total size of virtual memories can be greater than the physical memory
  - Provide greater support for multiprocessing

---
Thank you